## Slide 1: ECE 553: TESTING AND TESTABLE DESIGN OF DIGITAL SYSTEMS
General Introduction

## Slide 2: Outline
Introduction
  What is Testing
  Why is Testing Important
Types of Testing
Test Quality
Test Economics
Conclusions

## Slide 3: What is Testing?
Testing
Manufacturing Process
Testing is process of determining whether a piece of hardware
  Functioning correctly (PASS) or defective (FAIL)
Why do we need to test Integrated Circuits (ICs)?
  Because defects occur in manufacturing process
Pass:
Shippping
Fail: Reject
Defects
Testing is a Decision

## Slide 4: Four Possible Outcomes
True pass and true reject are correct decision
Test escapes = defective chips that pass test
  also known as (aka.) under-testing
Yield loss = good chips that fail the tests
Goal of good testing: reduce both test escape and yield loss
  Trade off between test cost and test quality
 | Good IC | Defective IC
Pass tests | True PASS | Test Escapes (less is better)
Fail tests | Yield Loss (less is better) | True Reject
Notes: Higher quality test means chips which pass the test are not defective. It does result in some good chips to fail the test and make the yield worse.
Higher quality means more cost.

## Slide 5: Quiz
Q: Which of following is NOT IC testing?
A: Run SPICE simulation on amplifier design to check if output is correctly amplified
B: Apply analog signal to an ADC IC and check if output is correctly digitized
C: Apply two numbers to an adder IC and check if output number is correctly added
Notes: Need physical IC so A is the answer.

## Slide 6: Outline
Introduction
  What is Testing?
  Why is Testing Important?
Types of Testing
Test Quality
Test Economics
Conclusions

## Slide 7: Stages of IC Product
Design
Verification
Fabrication
Prototype Test
Mass Production
Production Test
Customer
Diagnosis
Failure Analysis
Debug
feedback
good IC
returned IC
failing IC
diagnosed faults
Pictures of defects
& their root causes
feedback to design,
test & fab
Good Testing is Key to Success
pass test
fail test

## Slide 8: Why is Testing Important?
1. Guarantee IC quality
  Reduces test escapes
2. Shorten Time to Market, for example by:
  Improve efficiency of production test
  Better diagnose defective IC to improve yield
3. Enhance Profit for example by:
  Fix defective chips if possible (like memory)
  Reduce yield loss
8

## Slide 9: Testing is Everyone’s Responsibility
EDA
Auto.Test Pat. Gen. Fault simulation
Design
Design for testability
Built-in self test
Fabrication
Yield improvement Systematic defect diag.
Test Engineer
Test cost reduction Test quality assurance
Test Service
ATE maintenance
Test data analysis
GOOD TESTING
9
Reliability
Burn-in Accelerated life test
Physical Failure Analysis
Diagnosis

## Slide 10: Introduction
What Is Testing
Types of Testing
Test Quality
Test Economics
Conclusions
10

## Slide 11: Types of Testing
Testing (generally speaking)
Design Verification
Explicit Testing
Implicit Testing Or On-line Testing
Characterization Test
Production Test
Reliability Test
Diagnosis Test
Gross Test
DC parametric Test
AC parametric Test
Boolean Test
Delay Test
Wafer Test
Package Test
IDDQ, VLV
Functional Test
System Test Burn-in Acc. Life test
don’t worry about names too much
11

## Slide 12: Types of Tests from A High-Level
(1) Design verification
Logic design errors, physical design errors
(2) Explicit testing : test for defects
  Mask problems, lithography problem
  Particles or scratches
  Bad manufacture recipe
(3) Implicit or online testing : test for failure due to external disturbance during normal operation
  Electromagnetic interference
  Alpha particles
  Power supply disturbance
Why so many types of tests?
Focus of class
12
Because There Are Many Different Problems!

## Slide 13: Types of Testing
Testing (generally speaking)
Design Verification
Explicit Testing
Implicit Testing Or On-line Testing
Characterization Test
Production Test
Reliability Test
Diagnosis Test
Gross Test
DC parametric Test
AC parametric Test
Boolean Test
Delay Test
Wafer Test
Package Test
IDDQ, VLV
Functional Test
System Test Burn-in Acc. Life test
These Topics Are NOT in This Course

## Slide 14: Design Verification
Specifications description in sentences or codes
Design Code/Netlist/ layout
Silicon
IC chips
Physical devices
Verification
  Purpose : check if design correctly implements specified behavior
  Done before manufacture to catch design errors (bugs)
  Approaches: simulation, formal verification, …
Different from explicit testing
  Explicit testing’s purpose: check if IC is functioning correct or is defective
  Explicit testing done after manufacture to catch defects
  Approaches: apply test patterns by tester, …
design manufacture
= ?
Verification
(for bugs)
= ?
Testing (for defects)

## Slide 15: Implicit or Online Testing
Purpose
  Check IC output correctness during normal operation
Also known as:
  Concurrent Error Detection (CED)
  Online testing
Important for mission critical systems
  Airplanes, satellites, mainframe computers
Techniques (covered in courses related to fault-tolerant systems)
  Circuit level techniques
 Error Correction Code (ECC) protection of memory
  System level techniques
 Watch dog timer

## Slide 16: Types of Testing
Testing (generally speaking)
Design Verification
Explicit Testing
Implicit Testing Or On-line Testing
Characterization Test
Production Test
Reliability Test
Diagnosis Test
Gross Test
DC parametric Test
AC parametric Test
Boolean Test
Delay Test
Wafer Test
Package Test
IDDQ, VLV
Functional Test
System Test Burn-in Acc. Life test
don’t worry about names too much
16
According to purpose
According to stage
According to test technique
Notes: According to stages
  Wafer test (aka. Wafer sort, wafer probe): on wafer
  Package test (aka. Final test): after packaging
  System test: in system

## Slide 17
Testing (generally speaking)
Verification |  |  | On-line Testing | 
Characterization Test |  |  |  | 
Design
Explicit Testing
Implicit Testing Or
Production Test
Reliability Test
Diagnosis Test
Gross Test
DC parametric Test
AC parametric Test
Boolean Test
Delay Test
Wafer Test
Package Test
IDDQ, VLV
Functional Test
System Test Burn-in Acc. Life test
don’t worry about names too much
Types of Testing

## Slide 18: Characterization Tests
Test a small amount of prototype ICs very thoroughly
  Test cost and test time are not big concerns
Purpose of characterization test
  1. Verify IC function is same as design (silicon debug)
  2. Confirm IC specifications under different test conditions
 Specifications: speed, VOH/VOL, rise/fall time …
 Conditions: VDD, Temperature …
  3. Characterization test helps develop test program for production test
 Determine Pass/Fail limits
Notes: Determine pass/fail limits to ensure we have acceptable yield

## Slide 19: Shmoo Plot
VLSI Test 1.2 © N
Graphical display of CUT test results under different test conditions
Example: clock period (X-axis) vs. VDD (Y-axis)
  Green = PASS ; Red = FAIL
PASS
FAIL
Notes: Shows results of characterization test
Very time consuming because each rectangle is a test so we need mxn different tests

## Slide 20
Testing (generally speaking)
Design Verification
Explicit Testing
Implicit Testing Or On-line Testing
Characterization Test
Production Test
Reliability Test
Diagnosis Test
Gross Test
DC parametric Test
AC parametric Test
Boolean Test
Delay Test
Wafer Test
Package Test
System Test
Burn-in
IDDQ, VLV
Functional Test
Acc. Life test
don’t worry about names too much
Types of Testing

## Slide 21: Reliability Tests
Burn-in
  Goal: screen out early-life failure
  Method: raised temperature and voltage for hours or days
 cook IC in oven!
  Very costly. Only applied to expensive IC such as CPU
Accelerated Life Test (ALT)
  Goal: estimate life time of IC to estimate wear-out
  Method: burn-in until IC is dead
  Only applied to some sampled ICs
Burn-in oven siliconfareast.com
Burn-in board
Notes: Only to small sample because it is done until ICs are dead.
Reliability testing (type of explicit testing) : test for wear out
  Electromigration
  Corrosion

## Slide 22: Bathtub Curve
IC’s failure rate* resembles a bathtub
  Early-life failure: fail early in life, due to reliability defects
  Wear out: normal life time, due to aging
Failure rate
Early-life failure period
Normal
lifetime
Wear-out
period
~ 20 weeks
Burn-in
5 – 25 yrs
ALT
*Failure Rate = percentage of failures in a period of time
Time
Notes: High failure rate in first 20 weeks is due to ICs that escaped reliability test after production test.
Burn-in test help screen out the bad chips.
ALT: accelerated life test is needed to know the curve shape

## Slide 23
Testing (generally speaking)
Design Verification
Explicit Testing
Implicit Testing Or On-line Testing
Characterization Test
Production Test
Reliability Test
Diagnosis Test
Gross Test
DC parametric Test
AC parametric Test
Boolean Test
Delay Test
Wafer Test
Package Test
IDDQ, VLV
Functional Test
System Test Burn-in Acc. Life test
don’t worry about names too much
23
Types of Testing

## Slide 24: Production Tests
Purposes:
  1. Enforce quality requirements before selling to customers
  2. Sort parts for different specifications
 e.g. different speeds of CPU
Example: a typical production test flow
Wafer
Wafer Sort
Laser Repair
Packaging
Post-BI Test
Burn-In (BI)
Pre-BI Test
Final Test
Visual Inspection
QA Sample Test
Marking
Shipping
Notes: We mark ICs according to speed
A small amount of sampled ICs will be tested to ensure quality

## Slide 25: Production Test Floor
VLSI Test 1.2 © Nati
Yellow = Attention Needed
Green = PASS
Red = FAIL
Source: micron.com
Notes: Many testers and handlers. CUT are inside the handlers.
3 color light indicates test status.

## Slide 26
Testing (generally speaking)
Design Verification
Explicit Testing
Implicit Testing Or On-line Testing
Characterization
Test
Production Test
Reliability Test
Diagnosis Test
Gross DC parametric Test Test
21
AC parametric Test
Boolean Test
Delay Test
Wafer Test
Package Test
System Test
Burn-in
IDDQ, VLV
Functional Test
Acc. Life test
don’t worry about names too much
Types of Testing

## Slide 27: Wafer Test Setup
Source: Verigy.com
Probe station
ATE
Test head
wafer and probe card
Notes: Test head is now facing down
Many wafers stored in the probe station and each time pass one.

## Slide 28: Wafer Sort / Map
Why we call it wafer sort?
Wafer map shows test results
  Dies are sorted into different Bins
Example:
  Bin #1: PASS ALL
  BIN #2: FAIL FUNCTION test
  BIN #3: FAIL IDDQ test
  BIN #4: FAIL DC parametric test
Wafer map very useful for
  pass/fail decision
  diagnosis
  yield improvement
Yield=Bin#1/total = 78/130=60%

## Slide 29: Summary
Focus of this course: explicit testing
  Off-line IC testing on a specialized tester
  Explicit testing verification on-line testing
Many different types of tests for different
  Purposes
  Stages
Techniques
Testing (generally speaking)
Design
Verification
Explicit Testing
Implicit Testing Or
On-line Testing
Characterization Test
Production Test
Reliability Test
Diagnosis Test
Wafer Test Package Test System Test
Burn-in
Gross | DC parametric | AC parametric | Boolean | Delay Test | Functional | IDDQ,
Test | Test | Test | Test |  | Test | VLV
Acc. Life test