## Slide 1: ECE 553: TESTING AND TESTABLE DESIGN OF DIGITAL SYSTEMS
Fault Simulation

## Slide 2: Course Roadmap (EDA Topics)
2
Fault Simulation
Comb. ATPG
Seq. ATPG
Delay Test
Testability
Logic Sim. Fault Modeling
Diagnosis

## Slide 3: Motivating Problem
Apply 3 test patterns: P1, P2, P3: {0,1,0} {0,0,1} {1,0,0}
  Your manager asks you : What is fault coverage?

## Slide 4: Fault Simulation
Introduction
Fault simulation techniques

## Slide 5: What Is Fault Simulation?
Given:
  Circuit, fault model, test set
Determine:
  Output responses of faulty circuits
  Detected faults, Undetected faults
  Fault coverage
Commands
Fault Simulator
Good/Faulty Responses
Models (circuit, fault)
Input Stimuli (test set)
Fault coverage
detected faults

## Slide 6: Applications of Fault Simulation
1. Evaluate quality of test sets (aka. Fault Grading)
  Determine fault coverage of a test set
2. Automatic Test Pattern Generation (ATPG)
  Identify detected faults and undetected faults
3. Diagnosis
  Generate fault dictionary
  Find fault responsible for failure
Therefore, fault simulators can be used as either
  Stand alone tool, or
 Fault grading
  Embedded tool
 ATPG
 Diagnosis

## Slide 7: Fault Sim. Embedded in ATPG
After each test pattern generation
  Fault simulation
Fault dropping
  Remove detected faults from
fault list
  Prevent repeated test generation for detected faults
Pick a target
fault
Test pattern
generation
Fault Sim.
Fault Dropping
Any fault untried?
Yes
No
Finish
Fault Sim. Very Important for ATPG

## Slide 8: Fault Simulation
Introduction
Fault simulation techniques
  Serial fault simulation
  Parallel fault simulation (1965)
  PPSFP (1985)
  Deductive fault simulation (1972)

## Slide 9: Serial Fault Simulation
Simple Idea: Run a fault-free logic simulation, store good outputs
  For every fault
 Modify good circuit (fault injection) to obtain a faulty circuit
 Run logic simulation on faulty circuit
 Compare faulty outputs with stored good outputs
− fault is detected if they are different
Advantages
  Easy to implement (regular logic simulator).
  Ability to simulate many fault models (stuck-at, delay, …)
Disadvantage
  Long CPU time

## Slide 10: Quiz
Pat. | Input |  |  | Internal |  |  |  |  | Good Output
 | A | B | C | E | F | L | J | H | K
P1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1
P2 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
P3 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
-
P1
- P2
- P1
P3 P1 P1
- P1
P3 P3 P1
-
-
Q: Apply 3 test patterns: P1, P2, P3: {0,1,0} {0,0,1}
{1,0,0}. Please use serial fault simulation to determine fault coverage ? Consider all 18 faults.
A:
fault | Det. by | 
A/1 | P1 | 
A/0 | - | 
B/1 |  | 
B/0 |  | 
C/1 |  | 
C/0 |  | 
E/1 |  | 
E/0 |  | 
F/1 |  | 
F/0 |  | 
H/1 |  | 
H/0 |  | 
J/1 |  | 
J/0 |  | 
K/1 |  | 
K/0 |  | 
L/1 |  | 
L/0 |  | 
Notes: Fault coverage 11/ 18
Slow process

## Slide 11: Quiz
Pat. | Input |  |  | Internal |  |  |  |  | Output
 | A | B | C | E | F | L | J | H | K
P1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1
P2 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
P3 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
-
P1
- P2
- P1
P3 P1 P1
- P1
P3 P3 P1
-
-
Q: Apply 3 test patterns: P1, P2, P3: {0,1,0} {0,0,1}
{1,0,0}. Please use serial fault simulation to determine fault coverage ? Consider all 18 faults.
A:
fault | Det. by | 
A/1 | P1 | 
A/0 | - | 
B/1 |  | 
B/0 |  | 
C/1 |  | 
C/0 |  | 
E/1 |  | 
E/0 |  | 
F/1 |  | 
F/0 |  | 
H/1 |  | 
H/0 |  | 
J/1 |  | 
J/0 |  | 
K/1 |  | 
K/0 |  | 
L/1 |  | 
L/0 |  | 
Notes: Fault coverage 11/ 18
Slow process

## Slide 12: Complexity of Fault Simulation
12
Fault Simulation Complexity O(FxPxG)
  F: number of faults
  P: number of test patterns
  G: number of gates
Comparison
Logic simulation: O(G x P)
  ATPG: O(G x 2number_of_PI x F)
ATPG > Fault Sim > Logic Sim

## Slide 13: Fault Simulation
Introduction
Fault simulation techniques
  Serial fault simulation
  Parallel fault simulation (1965)
  PPSFP (1985) (parallel pattern)
  Deductive fault simulation (1972)
13

## Slide 14: Two Types of Parallelism
14
Exploit parallelism of logic instructions (bit-wise operations)
  1. Parallelism in faults
 Parallel Fault Simulation [Seshu 65]
  2. Parallelism in patterns
 Parallel Pattern Single Fault Propagation, PPSFP
[Wacukauski 85]

## Slide 15: Parallel Fault Simulation
[Seshu 65]
Run parallel logic simulation with W-1 faults (W determined by platform)
  one bit for fault-free circuit
  W-1 bits for faulty circuits assuming one fault in each circuit
(W-1) times faster than serial fault simulation (w/o fault dropping)
G | f1 | f2
fw-1
…
W bits
15

## Slide 16: Example
a sa0
b sa1
1 | 1 | 1
1
1
1
1 | 0 | 1
0
0
1
1 | 0 | 1
1
0
1
1 | 1 | 1
Assume W=3
Fault free
Circuit with only fault a
Circuit with only fault b
fault a detected
fault b not detected
16

## Slide 17: Fault Injection
VLSI Test 5.
Fault Injection = inserting fault(s) into circuit
Inserting a single fault is shown below
Control inputs of each fault should be set to activate it at the corresponding bit
a sa0
1 | 0 | 1
Control input
0 = SA0 fault injected
Quiz: how to insert SA1 fault? A:
Non-faulty case
17

## Slide 18: Fault Injection
How would it work to parallel simulate for multiple single stuck-at fault, assuming one SSF present at a time?
  Modify circuit by injecting all the fault s
  The size of each control input is k for k-1 injected faults (k-1 fault value + 1 fault free value)
  Parallel simulate (at each gate) based on the k-bit vector of each of its fanins
18

## Slide 19: Quiz
Q: Consider two faults: (A=SA1 , J=SA0). Use
parallel fault simulation on patterns
P1= {010},
P2= {001},
P3= {100}.
A:
19
Circuit is drawn after fault injection (injected faults are shown in grey)
Non-faulty
(non-controlling value)
A=SA1
J=SA0 (non-controlling value)
Notes: Circuit is modified to inject two faults (A SA1 and J SA0) show in grey

## Slide 20: Solution
Q: Consider two faults: (A=SA1 , J=SA0). Use
parallel fault simulation on patterns
P1= {010},
P2= {001},
P3= {100}.
A:
P1 P2 detect f P3 detects g
1 | 1 | 1
0 0 0
0 | 0 | 0
0 | 1 | 0
0 | 1 | 0
1 0 1
0 0 0
1 1 1
0 | 0 | 0
1 1 1
0 | 0 | 0
0 | 1 | 0
0 | 1 | 0
1 0 1
0 0 0
1 1 1
0 | 0 | 0
1 | 1 | 1
1 | 1 | 1
0 | 0 | 0
0 0 1
P1
20
P2
P3
0 0 0
0 0 0
1 1 0

## Slide 21: Fault Simulation
Introduction
Fault simulation techniques
  Serial fault simulation
  Parallel fault simulation (1965)
  PPSFP (1985) (parallel pattern)
  Deductive fault simulation (1972)
21

## Slide 22: PPSFP: Parallel Pattern Single Fault Propagation
Procedure
  Step 0: run logic simulation, store good output Og
  Step 1: Inject f1 by creating an event at the fault site
  Step 2: Perform event-driven simulation, get output Of1
 Compare Og and Of1
  Step 3. Create an event to undo fault effect of f1
 Inject an event for next fault f2
  Repeat step 2~3 until all faults simulated
W test patterns
Fault-free circuit
Out response Og
W test patterns
Out response Of1
W test patterns
Out response Of2
f
1
’
f
2
f1 X
22
X

## Slide 23: PPSFP Example
Assume W=3
Fault-free circuit
  Fault-free output 111 stored
1 | 0 | 1
1 | 0 | 0
1 | 0 | 0
0 | 1 | 1
1 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Pattern 1
Pattern 2
Pattern 3

## Slide 24: Example- cont’d
Fault a detected by P1
1 | 1 | 1
One event created to inject fault a
  fault effects are then propagated
Good =
1 | 0 | 1
1 | 0 | 0
0 | 0 | 0
0 | 1 | 1
0 | 1 | 1
0 | 0 | 0
a sa0
no event

## Slide 25: Example – cont’d
Fault b not detected
1 | 1 | 1
Two events created:
  One event to restore fault a
  One event to inject fault b
Good =
1 | 0 | 1
1 | 0 | 0
1 | 0 | 0
1 | 1 | 1
1 | 1 | 1
1 | 0 | 0
b sa1
Fault a restored
o

## Slide 26: Quiz
Q: Consider two faults: (f=SA1 , g=SA0). Use
PPSFP on patterns
P1= {010},
P2= {001},
P3= {100}.
A:

## Slide 27: Solution
2 ©
N
1 0 0
0 | 1 | 0
0 | 0 | 1
0 | 0 | 1
0 | 0 | 0
0 | 0 | 1
1 | 1 | 0
1 | 1 | 1
1 | 1 | 0
0 | 0 | 1
0 | 0 | 0
1 1 1
0. 0
0
Good
1 1 0
f
g
Q: Consider two faults: (f=SA1 , g=SA0). Use
PPSFP on patterns
P1= {010},
P2= {001},
P3= {100}.
A:
P1 P2 detect f P3 detects g
0 0 0
27

## Slide 28: Comparison
Serial fault simulation: one fault, one pattern
Parallel fault simulation: multiple faults, one pattern
PPSFP: multiple patterns, one fault
 | P1 | P2 | P3 | …
f1 |  |  |  | 
f2 |  |  |  | 
f3 |  |  |  | 
… |  |  |  | 
 | P1 |  |  | P2 |  |  | P3 |  |  | …
f1 |  |  |  |  |  |  |  |  |  | 
f2 |  | W-1 |  |  | W-1 |  |  | W-1 |  | 
f3 |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  | 
 | P1 |  | P2 | P3 | … | 
f1 |  |  |  |  |  | 
 |  | W |  |  |  | 
f2 |  |  |  |  |  | 
 |  | W |  |  |  | 
f3 |  |  |  |  |  | 
 |  | W |  |  |  | 
… |  |  |  |  |  | 

## Slide 29: Summary
Parallel fault simulation (parallel in fault)
  Run parallel logic simulation for W-1 faults
  Fault injection by circuit modification
Parallel Pattern Single fault Propagation (parallel in pattern)
  Run parallel logic simulation for W patterns

## Slide 30: Fault Simulation
Introduction
Fault simulation techniques
  Serial fault simulation
  Parallel fault simulation (1965)
  PPSFP (1985)
  Deductive fault simulation (1972)

## Slide 31: Deductive Fault Simulation
Procedure to apply one test pattern (P) at a time but consider a set of single-stuck-at faults (SSFs) in one shot
SSFs are given, e.g., for each line a stuck at fault opposite to its simulation value from P is assumed
For P, first perform a fault-free simulation
Gates are visited from PI to PO to create a "fault list" at (output of) each gate
  Fault list of a gate represents the set of all SSFs that are detected at the gate by P
  Creating the fault list of gate depends on the gate type, its input pin values (based on P), and fault lists at each of its input pins
The fault list at PO represents all faults that are detected by P
Uses logic deduction instead of simulation

## Slide 32: Deductive Fault Simulation
a = 0 La = {a/1}
b = 1 Lb = {b/0}
c = 0
Lc = {a/1, c/1}
d = 0
Ld = {a/1, c/1 , d/1}
e = 0
Le = {a/1, c/1 , e/1}
Pattern is ab=[01]
Assume SSFs: a/1, b/0, c/1, d/1, e/1
Detected faults are those in the fault lists of the POs
Eliminates per fault simulation

## Slide 33: Deductive Fault Simulation [Armstrong 72]
Li : Fault list of signal i
  Fault f Li , if i’s value changes in the presence of f
Fault list propagation example (for pattern ab=01)
  Assume SSF at each location opposite to its fault-free simulation value for pattern ab=01
  At primary inputs create La and Lb
a = 0
La = {a/1}
b = 1
Lb = {b/0}
c = 0
d = 0
e = 0
33

## Slide 34: Deductive Fault Simulation [Armstrong 72]
Li : Fault list of signal i
  Fault f Li , if i’s value changes in the presence of f
To compute Lc :
  a/1 in La is “propagated” to Lc
    Since b=1, c is changed from 0 to 1 when a/1
  b/0 in Lb is NOT propagated to Lc
    Since a=0, c is unchanged (remains c=0) when b/0
a = 0
La = {a/1}
b = 1
Lb = {b/0}
c = 0
Lc = {a/1, c/1}
d = 0
e = 0
34

## Slide 35: Deductive Fault Simulation [Armstrong 72]
Li : Fault list of signal i
  Fault f Li , if i’s value changes in the presence of f
To compute Ld and Le
  Propagate fault list from stem (Lc ) to each branch and add a new fault corresponding to the branch
a = 0
La = {a/1}
b = 1
Lb = {b/0}
c = 0
Lc = {a/1, c/1}
d = 0
Ld = {a/1, c/1 , d/1}
e = 0
Le = {a/1, c/1 , e/1}
35

## Slide 36: Example (P1)
Assume 18 uncollapsed faults for pattern P1 : ABC=010
  From the 18 faults, only SSFs which are opposite of pattern value at each line are relevant (rest cannot be detected by P1) : for example, for A=0 only A/1 is relevant and A/0 cannot be detected
(WWW Fig 3.26)
7 faults are detected by P1 ={010}
  Detected faults are dropped
  18-7=11 faults remains

## Slide 37: Example (P2)
Detected by P1: {A/1, H/1, B/0, E/0, F/0, J/1, K/0}, P2: ABC = 001
One more fault is detected by P2 = {001}
  Q: why no A/1?
  Answer: it was detected by P1 so it is dropped
11-1=10 faults remains
{C/0, L/0}

## Slide 38: Example (P3)
Detected so far: {A/1, H/1, B/0, E/0, F/0, J/1, K/0, C/0}, P3: ABC = 100
38
To determine LK, visit each fault in each of the two fault lists:
  For a given fault such as B/1 in LH
    B/1 in LH  H changes from 0 to 1 in presence of B/1
    B/1 in LJ  J changes from 1 to 0 in presence of B/1
    H=1 and J=1 --> K=0 (due to B/1) which is same as K=0 (fault-free case)  B/1 does not propagate to LK
{B/1, C/1, E/1, L/1}
F/1

## Slide 39: Example (P3)
Detected so far: {A/1, H/1, B/0, E/0, F/0, J/1, K/0, C/0}, P3: ABC = 100
39
To determine LK, visit each fault in each of the two fault lists:
  For another fault such as F/1 in LJ
    F/1 is not in LH  H remains 0 (non-controlling)
    F/1 is not in LJ  J changes from 1 to 0
    H=0, J=0  K=1 (for F/1) which is different than K=0 (fault-free case)  F/1 propagates to LK
{B/1, C/1, E/1, L/1}
F/1

## Slide 40: Example (P3)
Detected so far: {A/1, H/1, B/0, E/0, F/0, J/1, K/0, C/0}, P3: ABC = 100
Three more faults are detected by P3 = {100}
10-3=7 faults remains undetected
Fault Coverage = 11/18 = 61%
{B/1, C/1, E/1, L/1}
40
F/1
(WWW Fig 3.28)

## Slide 41: Fault List Propagation Rules (no need to know)
a b
c
a
b
c
∩ = set intersection; ∪= set union ; A-B = remove (A∩B) from A
a
c
Notes: Example: a=0 b=0 in AND  output fault list includes all faults that set a=1 (La) AND b=1 (Lb) at the same time (so intersection)
Example: a=0 b=1 in AND gate
Output fault list includes all faults that set a=1 (La) which are not setting b=0 (-Lb) .
Example: a=1 b=1  output fault list includes all faults that set a=0 (La) AND/OR b=0 (Lb) (so union)

## Slide 42: Summary
42
Idea: Use logic deduction instead of simulation
Advantages
  No loop of faults
Disadvantages
 Problem with calculating fault propagation lists
 Very complicated rules depending on situation
 Difficult memory management
 Memory requirement not predictable
 Many ∩ ∪ operations difficult for large designs

## Slide 43: References
[Abramovici 1984] M. Abramovici, P. R. Menon, and D. T. Miller, “Critical Path Tracing: An Alternative to Fault Simulation,” IEEE Design and Test of Computers, 1984.
[Armstrong 1972] D. B. Armstrong, A deductive method for simulating faults in logic circuits, IEEE Trans. Comput., C-21(5), 464–471, 1972.
[Butler 1974] T. T. Butler, T. G. Hallin, J. J. Kulzer, and K. W. Johnson, LAMP: Application to switching system development, Bell System Tech. J., 53, 1535–1555, 1974.
[Cheng 1989] W. T. Cheng and M. L. Yu, Differential fault simulation: A fast method using minimal memory, in Proc. Des. Automat. Conf., June 1989, pp. 424–428.
[Jain 1985] S. K. Jain and V. D. Agrawal, Statistical fault analysis, IEEE Des. Test Comput., 2(1), 38–44, 1985.
[Seshu 1965] S. Sesuh and D. N. Freeman, On improved diagnosis program, IEEE Trans. Electron. Comput., EC-14(1), 76–79, 1965.
[Ulrich 1974] E. G. Ulrich and T. Baker, Concurrent simulation of nearly identical
digital networks, IEEE Trans. Comput., 7(4), 39–44, 1974.
[Waicukauski 1985] J. A. Waicukauski, E. B. Eichelberger, D. O. Forlenza, E. Lindbloom, and T. McCarthy, Fault simulation for structured VLSI, Proc. VLSI Syst. Des., 6(12), 20–32, 1985.
43